## Slide 1: Computer Organization & Design The Hardware/Software Interface
计算机组成与设计
Chapter 3
Arithmetic for Computer

## Slide 2: Contents of Chapter 3
3.1 Introduction
3.2 Signed and Unsigned Numbers-Possible Representations
3.3 Arithmetic--Addition & subtraction and ALU
3.4 Multiplication
3.5 Division
3.6 Floating point numbers

## Slide 3: 3.1 Introduction
Computer words are composed of bits;
  thus words can be represented as binary numbers
  there are 32bits/word or 64bits/word in RISC-V
  Contains four bytes for 32bits word
Simplified to contain only in course:
  memory-reference instructions: lw, sw
  arithmetic-logical instructions: add, sub, and, or, xor, slt…
  control flow instructions: beq, bne, jal
Generic Implementation:
  use the program counter (PC) to supply instruction address
  get the instruction from memory
  read registers
  use the instruction to decide exactly what to do
All instructions use the ALU after reading the registers Why? memory-reference? arithmetic? control flow?

## Slide 4: Numbers
Bits are just bits (no inherent meaning)— conventions define relationship between bits and numbers
Binary numbers (base 2) 0000 0001 0010 0011 0100 0101 0110 0111 1000 1001... decimal: 0 1 2 3...2n-1
Of course it gets more complicated: numbers are finite (overflow) fractions and real numbers negative numbers
How do we represent numbers? i.e., which bit patterns will represent which numbers?

## Slide 5: Do you Know?
What is this about following Digital?
001100111101111000000001000000002
  Don’t know! (Do not know, is the right answer !)
Ah, Why?
  Because different occasions have different meaning
The possible meaning is
  IP Address
  Machine instructions
  Values of Binary number :
    Integer
    Fixed Point Number
    Floating Point Number

## Slide 6: For binary integer
The following 4-bit binary integer What does it mean?
10012
  Don’t know!
Ah, still do not know for?
Integer representation of different methods have different meaning
  Unsigned 10012=910
  Signed 10012=-110 or -710 ?
  Do not know, is the right answer !

## Slide 7: 3.2 Signed and Unsigned Numbers Possible Representations
Sign Magnitude: One's Complement Two's Complement 000 = +0 000 = +0 000 = +0 001 = +1 001 = +1 001 = +1 010 = +2 010 = +2 010 = +2 011 = +3 011 = +3 011 = +3 100 = -0 100 = -3 100 = -4 101 = -1 101 = -2 101 = -3 110 = -2 110 = -1 110 = -2 111 = -3 111 = -0 111 = -1
Which one is best? Why?
  Issues: number of zeros, ease of operations

## Slide 8: Numbers and their representation
Number systems
  Radix based systems are dominating
  decimal, octal, binary,…
  A: value of the digit, k: radix, n: digits left of radix point, m: digits right of radix point
  Alternatives, e.g. Roman numbers (or Letter)
Decimal (k=10) → used by humans
Binary (k=2) → used by computers
0≤A≤K
(N)k＝(An－1A n－2A n－3…A 1A 0 • A-1A -２A…A –m+1A – m)k
MSD
LSD
Notes: Radix =基数
罗马数字共有7个，即Ⅰ(1)，Ⅴ(5)，Ⅹ(10)，Ⅼ(50)，Ⅽ(100)，Ⅾ(500)，Ⅿ(1000)。需要注意的是罗马数字中没有“0”。

## Slide 9: Numbers and their representation
Representation
  ASCII - text characters
    Easy read and write of numbers
    Complex arithmetic (character wise)
  Binary number
    Natural form for computers
    Requires formatting routines for I/O

## Slide 10: Number types
Integer numbers, unsigned
  Address calculations
  Numbers that can only be positive
Signed numbers
  Positive
  Negative
Floating point numbers
  numeric calculations
  Different grades of precision
    Singe precision (IEEE)
    Double precision (IEEE)
    Quadruple precision

## Slide 11: Number formats
Sign and magnitude
2's complement
1's complement
similar to 2's complement, + 0 & - 0
Biased notation
1000 0000 = minimal negative value(-27)
0111 1111 = maximal positive value (27-1)
Representation
  Binary
  Decimal
  Hexadecimal
Notes: 移码，加上2^n

## Slide 12: Signed number representation
First idea:
  Positive and negative numbers
  Take one bit (e.g. 31) as the sign bit
    Problem
    0 0000000 = 0 positive zero!
    1 0000000 = 0 negative zero!
  Each comparison to 0 requires two steps
1's complement
2's complement

## Slide 13: Two's Complement Operations
Negating a two's complement number:
invert all bits & add 1 with end
  remember: “negate” and “invert” are quite different!
Defining : Assume:x＝±0.x-1x-２x-３…x-m OR x＝±xn-1x-n-２x-n-３x-n-4…x-0
Converting n bit numbers into numbers with more than n bits:
  MIPS 16 bit immediate gets converted to 32 bits for arithmetic
  copy the most significant bit (the sign bit) into the other bits 0010 -> 0000 0010 1010 -> 1111 1010
Ｘ 0≤X<1
２＋Ｘ＝2－|Ｘ| -1≤X<0
Ｘ 0≤X<2n
2n+1＋Ｘ＝2n+1－|Ｘ| -2n≤X<0
fraction
integer
[X]C＝
Notes: Negative: 负数

## Slide 14: 2's complement for n=3
Only one representation for 0
One more negative number than positive number
2n+1＋Ｘ＝2n+1-|Ｘ|
＝ 24 －8
＝(10000-1000)2
＝ 01000
0 100 =+4
1 100 =-4
The absolute value of the sum of two=2n

## Slide 15: More common: use of 2's complement ---- negatives have one additional number
  (0000 0000 0000 0000 0000 0000 0000 0000)2 =(0)10
  (0000 0000 0000 0000 0000 0000 0000 0001)2 =(1)10
  ………… ………
  (0111 1111 1111 1111 1111 1111 1111 1101)2 =( 2，147，483，645)10
  (0111 1111 1111 1111 1111 1111 1111 1110)2 =( 2，147，483，646)10
  (0111 1111 1111 1111 1111 1111 1111 1111)2 =( 2，147，483，647)10
  (1000 0000 0000 0000 0000 0000 0000 0000)2 =(-2，147，483，648)10
  (1000 0000 0000 0000 0000 0000 0000 0001)2 =(-2，147，483，647)10
  (1000 0000 0000 0000 0000 0000 0000 0010)2 =(-2，147，483，646)10
  ………… ………
  (1111 1111 1111 1111 1111 1111 1111 1101)2 =(-3)10
  (1111 1111 1111 1111 1111 1111 1111 1110)2 =(-2)10
  (1111 1111 1111 1111 1111 1111 1111 1111)2 =(-1)10
Notes: -1就是全1，最大的负数是100000.。。000

## Slide 16: Two's Biased notation
Negating Biased notation number:
invert all bits and add 1 with end
Defining : Assume: x＝±x-(n-1)x-(n-２)x-(n-３)x-(n-4)…x-0
X=＋1011 [X]b=11011 sign bit “1” Positive X=－1011 [X]b=00101 sign bit “0” Negative
2's Biased notation VS 2's complement
  Only reverse sign bit
  e.g.
  X=＋1011 [X]c=01011 [X]b=11011
X=－1011 [X]c=10101 [X]b=00101
[X]b＝ 2n＋Ｘ -2n≤X ≤ 2n
[0]b ＝100000…(2n)
IEEE 754: [X]b＝ 2n-1＋Ｘ
biase

## Slide 17: sign extension (lbu vs. lb)
Expansion
e.g. 8 bit numbers to 64/32 bit numbers
Required for operations with registers(32/64 bits) and immediate operands (8 bits)
Sign extension
  Take the lower 8 bits as they are
  Copy the highest bit to the remaining 24/56 bits
  0000 0010 → 2
  0000 0000 0000 0000 0000 0000 0000 0010
  1111 1110 → -2
  1111 1111 1111 1111 1111 1111 1111 1110

## Slide 18: 3.3 Arithmetic
Addition and Subtraction
Logical operations
Constructing a simple ALU
Multiplication
Division
Floating point arithmetic
Adding all parts to get an ALU

## Slide 19: Addition & subtraction
Adding bit by bit, carries → next digit
  0000 0111 710
  + 0000 0110 610
  0000 1101 1310
Subtraction
  Directly
  Addition of 2's complement
  0000 0111 710
  - 0000 0110 610
  0000 0001 110
  0000 0111 710
  + 1111 1010 -610
  0000 0001 110

## Slide 20: Overflow
The sum of two numbers can exceed any representation
The difference of two numbers can exceed any representation
2's complement:
Numbers change
sign and size
Notes: 同号数相加或者异号数相减， 可能发生溢出。

## Slide 21: Overflow conditions
General overflow conditions
Operation | Operand A | Operand B | Result overflow
A+B | ≧0 | ≧0 | <0 (01)
A+B | <0 | <0 | ≧0 (10)
A-B | ≧0 | <0 | <0 (01)
A-B | <0 | ≧0 | ≧0 (10)
Double sign-bits

## Slide 22: Reaction of Overflow
An exception (interrupt) occurs
  Control jumps to predefined address for exception
  Interrupted address is saved for possible resumption
Signaling to application (Ada, Fortran)
Ignore, don't always want to detect overflow note: sltu, sltiu for unsigned comparisons

## Slide 23: Overflow process
Hardware detection in the ALU
  Generation of an exception (interrupt)
Save the instruction address (not PC) in special register SEPC
Jump to specific routine in OS
  Correct & return to program
  Return to program with error code
  Abort program

## Slide 24: Arithmetic for Multimedia
Graphics and media processing operates on vectors of 8-bit and 16-bit data
  Use 64-bit adder, with partitioned carry chain
    Operate on 8×8-bit, 4×16-bit, or 2×32-bit vectors
  SIMD (single-instruction, multiple-data)
Saturating operations
  On overflow, result is largest representable value
    c.f. 2s-complement modulo arithmetic
  E.g., clipping in audio, saturation in video

## Slide 25: Logical operations
Logical shift operations
  right (srl)
  left (sll)
The machine instruction for the instruction slli x11, x9, 3
Example: slli x11, x9, 3
  x9: 0000 0000 0000 0000 1100 1000 0000 1111
  x11: 0000 0000 0000 0110 0100 0000 0111 1000
Op | Rs | Rt | Rd | Shamt | Adr/funct
0 | 0 | 16 | 10 | 3 | 0
Filled with '0'

## Slide 26: Logical operations skip
AND→bit-wise AND between registers
and register1, register2, register3
OR →bit-wise OR between registers
or register1, register2, register3
Example:
and x3, x10, x16
or x4, x10, x16
  x16: 0000 0000 0000 0000 1100 1000 0000 1111
  x10: 0000 0000 0000 0110 0100 0000 0111 1000
  x3: 0000 0000 0000 0000 0100 0000 0000 1000
  x4: 0000 0000 0000 0110 1100 1000 0111 1111

## Slide 27: Constructing an ALU
Two methods constitute the ALU
  extended the adder
  Parallel redundant select
Step by step:
  build a single bit ALU
  and expand it to the desired width
First function:
  logic AND and OR

## Slide 28: A half adder
Sum = b + a
Carry = a b

## Slide 29: A full adder
Accepts a carry in
Sum = A + B + CarryIn
CarryOut = B CarryIn + A CarryIn + A B
Inputs |  |  | Outputs |  | Comments
A | B | CarryIn | CarryOut | Sum | 
0 | 0 | 0 | 0 | 0 | 0+0+0=00
0 | 0 | 1 | 0 | 1 | 0+0+1=01
0 | 1 | 0 | 0 | 1 | 0+1+0=01
0 | 1 | 1 | 1 | 0 | 0+1+1=10
1 | 0 | 0 | 0 | 1 | 1+0+0=01
1 | 0 | 1 | 1 | 0 | 1+0+1=10
1 | 1 | 0 | 1 | 0 | 1+1+0=10
1 | 1 | 1 | 1 | 1 | 1+1+1=11

## Slide 30: Full adder Logic circuit
Full adder in 2-level design
+

## Slide 31: 1 bit ALU
ALU
  AND
  OR
  ADD
Cell Cascade Element

## Slide 32: Basic 32 bit ALU
Inputs parallel
Carry is cascaded
Ripple carry adder
行波进位加法器
Slow, but simple
1st Carry In = 0

## Slide 33: Extended 1 bit ALU-- Subtraction
Subtraction
a - b
  Inverting b
  1st CarryIn= 1

## Slide 34: Extended 1 bit ALU-- comparison
Functions
  AND
  OR
  Add
  Subtract
Missing: comparison
  slt rd,rs,rt
  If rs < rt, rd=1, else rd=0
  All bits = 0 except the least significant
  Subtraction (rs - rt), if the result is negative→ rs < rt
  Use of sign bit as indicator

## Slide 35
Most significant bit
  Set for comparison
  Overflow detect
Cell Cascade Element
Most
significant bit
Last
significant bit
Operation | Operand A | Operand B | Result overflow
A+B | ≧0 | ≧0 | <0 (01)
A+B | <0 | <0 | ≧0 (10)
A-B | ≧0 | <0 | <0 (01)
A-B | <0 | ≧0 | ≧0 (10)

## Slide 36: Complete ALU
Input
  A、B
Control lines
  Binvert
  Operation
  Carry in
Output
  Result
  Overflow
Slow, but simple
  Inputs parallel
  Carry is cascaded
    Ripple carry adder
Iterative Circuit

## Slide 37: Complete ALU —with Zero detector
Add a Zero detector

## Slide 38: ALU symbol & Control
Symbol of the ALU
Control：Function table
ALU Control Lines | Function
000 | And
001 | Or
010 | Add
110 | Sub
111 | Set on less than
100 | nor
101 | srl
011 | xor

## Slide 39: ALU Hardware Code
module alu(A, B, ALU_operation, res, zero, overflow );
input [31:0] A, B;
input [2:0] ALU_operation;
output [31:0] res;
output zero, overflow ;
wire [31:0] res_and,res_or,res_add,res_sub,res_nor,res_slt;
reg [31:0] res;
parameter one = 32'h00000001, zero_0 = 32'h00000000;
assign res_and = A&B;
assign res_or = A|B;
assign res_add = A+B;
assign res_sub = A-B;
assign res_slt =(A < B) ? one : zero_0;
always @ (A or B or ALU_operation)
case (ALU_operation)
3'b000: res=res_and;
3'b001: res=res_or;
3'b010: res=res_add;
3'b110: res=res_sub;
3'b100: res=~(A | B);
3'b111: res=res_slt;
default: res=32'hx;
endcase
assign zero = (res==0)? 1: 0;
endmodule
How do you write with overflow code ?
always @ (A or B or ALU_operation)
case (ALU_operation)
3'b000: res=A&B;
3'b001: res=A|B;
3'b010: res=A+B;
3'b110: res=A-B;
3'b100: res=~(A | B);
3'b111: res=(A < B) ? one : zero_0;
default: res=32'hx;
endcase
What is the difference The codes in the Synthesize?

## Slide 40: Speed considerations
Previously used: ripple carry adder
Delay for the sum: two units
Delay for the carry:
  two - three units
Ai
Bi
Ci
Ci+1
Gi
Pi
Si

## Slide 41: Speed considerations
Delay of one adder
  2 time units
Total delay for stages: 2n unit delays
Not appropriate for high speed application
A3
B3
S3
B2
S2
B1
S1
S0
B0
A2
A1
A0
C4
C3
C2
C1
C0

## Slide 42: Fast adders
All functions can be represented in 2-level logic.
But:
  The number of inputs of the gates would drastically rise
Target:
Optimum between speed and size

## Slide 43: Fast adders
Carry look-ahead adder
  Calculating the carries before the sum is ready
Carry skip adder
  Accelerating the carry calculation by skipping some blocks
Carry select adder
  Calculate two results and use the correct one
...

## Slide 44: Carry Lookahead Adder (CLA)
Given Stage i from a Full Adder, we know that there will be a carry generated when Ai = Bi = "1", whether or not there is a carry-in
Alternately, there will be a carry propagated if the “half-sum” is "1" and a carry-in, Ci occurs, then Ci+1=1
These two signal conditions are called
  generate, denoted as Gi
  propagate, denoted as Pi
Ai
Bi
Ci
Ci+1
Gi
Pi
Si
Notes:   gi = ai * bi
  pi = ai + bi

## Slide 45: Addition formula in CLA
In the ripple carry adder:
  Gi, Pi, and Si are local to each cell of the adder
  Ci is also local each cell
In the carry lookahead adder, in order to reduce the length of the carry chain, Ci is changed to a more global function spanning multiple cells
Defining the equations for the Full Adder in term of the Pi and Gi:
i
i
i
i
i
i
B
A
G
B
A
P
=
Å
=
i
i
i
1
i
i
i
i
C
P
G
C
C
P
S
+
=
Å
=
+

## Slide 46: Carry Lookahead Development
Ci+1 can be removed from the cells and used to derive a set of carry equations spanning multiple cells.
Beginning at the cell 0 with carry in C0:
C1 = G0 + P0 C0
C4 = G3 + P3 C3 = G3 + P3G2 + P3P2G1
+ P3P2P1G0 + P3P2P1P0 C0
C2 = G1 + P1 C1 = G1 + P1(G0 + P0 C0)
= G1 + P1G0 + P1P0 C0
C3 = G2 + P2 C2 = G2 + P2(G1 + P1G0 + P1P0 C0)
= G2 + P2G1 + P2P1G0 + P2P1P0 C0

## Slide 47: Carry Lookahead Adder
partial full adder
0
1
2
3
3
0
0
0
1
2
3
1
2
3
2
3
3
3
0
P
P
P
P
P
G
P
P
P
P
G
P
P
G
P
G
G
=
+
+
+
=
-
-

## Slide 48: Group Carry Lookahead Logic
Last slide show shows the implementation of these equations for four bits. This could be extended to more than four bits; in practice, due to limited gate fan-in, such extension is not feasible.
Instead, the concept is extended another level by considering group generate (G0-3) and group propagate (P0-3) functions:
Using these two equations:
Thus, it is possible to have four 4-bit adders use one of the same carry lookahead circuit to speed up 16-bit addition
0
1
2
3
3
0
0
0
1
2
3
1
2
3
2
3
3
3
0
P
P
P
P
P
G
P
P
P
P
G
P
P
G
P
G
G
=
+
+
+
=
-
-
0
3
0
3
0
4
C
P
G
C
-
-
+
=

## Slide 49: Extended Example: 16 carry lookahead adder
C4 = G3 + P3G2 + P3P2G1 + P3P2P1G0 + P3P2P1P0C0 = G0~3+ P0~3C0
C8 = G7 + P7G6 + P7P6G5 + P7P6P5G4 + P7P6P5P4C4 = G4~7+ P4~7C4
C12 =G11+P11G10+P11P10G9+P11P10P9G8+P11P10P9P8C8 = G8~11+ P8~11C8
C16=G15+P15G14+P15P14G13+P15P14P13G12+P15P14P13P12C12 = G12~15+ P12~15C12
= G12~15+ P12~15(G8~11+ P8~11(G4~7+ P4~7(G0~3+ P0~3C0)))
G0~3 = G3 + P3G2 + P3P2 G1 +P3P2P1G0
G4~7 = G7 + P7G6 + P7P6G5 + P7P6P5G4
G8~11 = G11+P11G10+P11P10G9+P11P10P9G8
G12~15= G15+P15G14+P15P14G13+P15P14P13G12
P0~3 = P3 P2 P1 P0
P4~7 = P7 P6 P5 P4
P8~11 = P11 P10 P9 P8
P12~15= P15 P14 P13 P12
C4 = G3 + P3G2 + P3P2G1 + P3P2P1G0 + P3P2P1P0 C0
CLA
CLA
CLA
CLA
CLA

## Slide 50: Carry skip adder
Accelerating the carry by skipping the interior blocks
Optimal speed with no-equal distribution of block length

## Slide 51: Carry skip adder

## Slide 52: Carry select adder (CSA)

## Slide 53: Carry select adder
Carry selection by nibbles

## Slide 54: 3.4 Multiplication
Binary multiplication
Multiplicand × Multiplier
1000 × 1001
Look at current bit position
  If multiplier is 1
    then add multiplicand
    Else add 0
  shift multiplicand left by 1 bit
 |  |  |  | 1 | 0 | 0 | 0
 |  |  | × | 1 | 0 | 0 | 1
 |  |  |  | 1 | 0 | 0 | 0
 |  |  | 0 | 0 | 0 | 0 | 
 |  | 0 | 0 | 0 | 0 |  | 
+ | 1 | 0 | 0 | 0 |  |  | 
 | 1 | 0 | 0 | 1 | 0 | 0 | 0
Notes: Multiplicand=被乘数 Multiplier=乘数

## Slide 55: Multiplier V1– Logic Diagram
64 bits: multiplier
128 bits: multiplicand, product, ALU
0010*0011
128
-
b
i
t
A
L
U
C
o
n
t
r
o
l
t
e
s
t
M
u
l
t
i
p
l
i
e
r
S
h
i
f
t
r
i
g
h
t
P
r
o
d
u
c
t
W
r
i
t
e
M
u
l
t
i
p
l
i
c
a
n
d
S
h
i
f
t
l
e
f
t
128
b
i
t
s
128
b
i
t
s
64 bits
0000 0110
0011
0000 0010

## Slide 56: Multiplier V1--Algorithmic rule
Requires 64 iterations
  Addition
  Shift
  Comparison
Almost 200 cycles
Very big, Too slow!
64th repetition?

## Slide 57: Multiplier V2
Real addition is performed only with 64 bits
Least significant bits of the product don't change
New idea:
  Don’t shift the multiplicand
  Instead, shift the product
  Shift the multiplier
ALU reduced to 64 bits!
 |  |  |  | 1 | 0 | 0 | 0
 |  |  | × | 1 | 0 | 0 | 1
 |  |  |  | 1 | 0 | 0 | 0
 |  |  | 0 | 0 | 0 | 0 | 
 |  | 0 | 0 | 0 | 0 |  | 
+ | 1 | 0 | 0 | 0 |  |  | 
 | 1 | 0 | 0 | 1 | 0 | 0 | 0

## Slide 58: Multiplier V2-- Logic Diagram
Diagram of the V2 multiplier
Only left half of product register is changed

## Slide 59: Multiplier V2----Algorithmic rule
Addition performed
only on left half of
product register
Shift of product register
64
64
64th repetiion?

## Slide 60: Revised 4-bit example with V2
Multiplicand x multiplier: 0001 x 0111
Multiplicand: | 0001 |  |  | 
Multiplier:× | 0111 |  |  | 
 | 0000 | 0000 |  | #Initial value for the product
1 | 0001 | 0000 |  | #After adding 0001, Multiplier=1
 | 0000 | 1000 | 0 | #After shifting right the product one bit
 | 0001 |  |  | 
2 | 0001 | 1000 |  | #After adding 0001, Multiplier=1
 | 0000 | 1100 | 0 | #After shifting right the product one bit
 | 0001 |  |  | #After adding 0001, Multiplier=1
3 | 0001 | 1100 |  | 
 | 0000 | 1110 | 0 | #After shifting right the product one bit
 | 0000 |  |  | 
4 | 0000 | 1110 |  | #After adding 0001, Multiplier=0
 | 0000 | 0111 | 0 | #After shifting right the product one bit
Shift out

## Slide 61: Multiplier V 3
Further optimization
At the initial state the product register contains only '0'
The lower 64 bits are simply shifted out
Idea: use these lower 64 bits for the multiplier
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 |  |  |  | 
0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 |  |  | 
0 | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 0 |  | 
0 | 0 | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 
0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 0
multiplier

## Slide 62: Multiplier V3 Logic Diagram
Notes: Product实际是129位，来保存加法器的进位。

## Slide 63: Multiplier V3--Algorithmic rule
Set product register to '0'
Load lower bits of product
register with multiplier
Test least significant bit of product register
64
64
64th repetiion?

## Slide 64: Example with V3
Multiplicand x multiplier: 0001 x 0111
Multiplicand: | 0001 |  |  | 
Multiplier:× | 0111 |  |  | 
 | 0000 | 0111 |  | #Initial value for the product
1 | 0001 | 0111 |  | #After adding 0001, Multiplier=1
 | 0000 | 1011 | 1 | #After shifting right the product one bit
 | 0001 |  |  | 
2 | 0001 | 1011 |  | #After adding 0001, Multiplier=1
 | 0000 | 1101 | 1 | #After shifting right the product one bit
 | 0001 |  |  | #After adding 0001, Multiplier=1
3 | 0001 | 1101 |  | 
 | 0000 | 1110 | 1 | #After shifting right the product one bit
 | 0000 |  |  | 
4 | 0000 | 1110 |  | #After adding 0001, Multiplier=0
 | 0000 | 0111 | 0 | #After shifting right the product one bit
Shift out

## Slide 65: Signed multiplication
Basic approach:
  Store the signs of the operands
  Convert signed numbers to unsigned numbers
  (most significant bit (MSB) = 0)
  Perform multiplication
  If sign bits of operands are equal
  sign bit = 0, else
  sign bit = 1
Improved method:
Booth's Algorithm
Assumption: addition and subtraction are available

## Slide 66: Principle -- Decomposable multiplication
Assumes： Z=y×10111100
Z=y(10000000+111100+100-100)
=y(1×27+1000000-100)
=y(1×27+1×26-22)
=y(1×27+1×26+0×25+0×24+0×23+0×22+0×21+0×20 -1×22 )
= y(1×27+1×26+0×25+0×24+0×23+0×22-1×22 +0×21+0×20)
= y×27+y×1×26+0×25+0×24+0×23 +0×22-y×22 +0×21+0×20)
Only shift
Only shift
add
sub
1 01 11 1 00

## Slide 67: Booth's Algorithm
Idea: If you have a sequence of '1's
  subtract at first '1' in multiplier
  shift for the sequence of '1's
  add where prior step had last '1‘
Result:
  Possibly less additions and more shifts
  Faster, if shifts are faster than additions

## Slide 68: Example for Booth's Algorithm
Logic required identifying the run

## Slide 69: Booth's Algorithm rule
Analysis of two consecutive bits
Action
      1 0 subtract multiplicand from left
      1 1 no arithmetic operation-shift
      0 1 add multiplicand to left half
      0 0 no arithmetic operation-shift
Bit-1 = '0'
Arithmetic shift right:
  keeps the leftmost bit constant
  no change of sign bit !

## Slide 70: Example with negative numbers
2 * (-3) = - 6
0010 * 1101 = 1111 1010
iteration | step | Multiplicand | product
0 | Initial Values | 0010 | 0000 1101 0
1 | 1.c:10→Prod=Prod-Mcand | 0010 | 1110 1101 0
 | 2: shift right Product | 0010 | 1111 0110 1
2 | 1.b:01→Prod=Prod+Mcand | 0010 | 0001 0110 1
 | 2: shift right Product | 0010 | 0000 1011 0
3 | 1.c:10→Prod=Prod-Mcand | 0010 | 1110 1011 0
 | 2: shift right Product | 0010 | 1111 0101 1
4 | 1.d: 11 → no operation | 0010 | 1111 0101 1
 | 2: shift right Product | 0010 | 1111 1010 1

## Slide 71: 13 * (-11) = - 143 -13= +10011 01101 * 10101 = 11011 10001-->00100 01111
 | step | Multiplicand | product
0 | Initial Values | 01101 | 00000 10101 0
1 | 1.c:10→Prod=Prod-Mcand | 01101 | 10011 10101 0
 | 2: shift right Product | 01101 | 11001 11010 1
2 | 1.b:01→Prod=Prod+Mcand | 01101 | 00110 11010 1
 | 2: shift right Product | 01101 | 00011 01101 0
3 | 1.c:10→Prod=Prod-Mcand | 01101 | 10110 01101 0
 | 2: shift right Product | 01101 | 11011 00110 1
4 | 1.d:01→Prod=Prod+Mcand | 01101 | 01000 00110 1
 | 2: shift right Product | 01101 | 00100 00011 0
 | 1.e:10→Prod=Prod-Mcand | 01101 | 10111 00011 0
 | 2: shift right Product | 01101 | 11011 10001 1

## Slide 72: Faster Multiplication
Uses multiple adders
  Cost/performance tradeoff
Can be pipelined
  Several multiplication performed in parallel

## Slide 73: RISC-V Multiplication
Four multiply instructions:
  mul: multiply
    Gives the lower 64 bits of the product
  mulh: multiply high
    Gives the upper 64 bits of the product, assuming the operands are signed
  mulhu: multiply high unsigned
    Gives the upper 64 bits of the product, assuming the operands are unsigned
  mulhsu: multiply high signed/unsigned
    Gives the upper 64 bits of the product, assuming one operand is signed and the other unsigned
  Use mulh result to check for 64-bit overflow

## Slide 74: 3.5 Division
Check for 0 divisor
Long division approach
  If divisor ≤ dividend bits
    1 bit in quotient, subtract
  Otherwise
    0 bit in quotient, bring down next dividend bit
Restoring division
  Do the subtract, and if remainder goes < 0, add divisor back
Signed division
  Divide using absolute values
  Adjust sign of quotient and remainder as required
1001
1000 1001010
-1000
10
101
1010
-1000
10
n-bit operands yield n-bit quotient and remainder
quotient
dividend
remainder
divisor

## Slide 75: Division V1 --Logic Diagram
At first, the divisor is in the left half of the divisor register, the dividend is in the right half of the remainder register.
Shift right the divisor register each step
Initially dividend
Initially divisor in left half
Dividend = quotient × divisor + remainder
  Remainder < divisor
  Iterative subtraction
Result:
  Greater than 0: then we get a 1
  Smaller than 0: then we get a 0

## Slide 76: Algorithm V 1
Each step:
  Subtract divisor
  Depending on Result
    Leave or
    Restore
  Depending on Result
    Write '1' or
    Write '0'

## Slide 77: Example (7÷ 2) for division v1 00000111 ÷0010
0000

## Slide 78: Two questions
1.Why should the divisor be shifted right one bit each time?
2.Why should the divisor be placed in the left half of the divisor register , and the dividend be placed in the right half of the remainder register at first ?
divisor
quotient
dividend
remainder
- divisor
- divisor
remainder
…………
0

## Slide 79: Modified Division
Reduction of Divisor and ALU width by half
Shifting of the remainder
Saving 1 iteration
Remainder register keeps quotient No quotient register required
dividend
One cycle per partial-remainder subtraction
Looks a lot like a multiplier!
  Same hardware can be used for both
Notes: 乘法和除法用同样的硬件结构可以实现

## Slide 80: Algorithm V 3
Much the same as
the last one
Except change of
register usage
64th repetition?
No: < 64th repetition
Yes: 64th repetition

## Slide 81: Example 7/2 for Modified Division
Well known numbers: 0000 0111/0010
iteration | step | Divisor | Remainder
0 | Initial Values | 0010 | 0000 0111
 | Shift Rem left 1 | 0010 | 0000 1110
1 | 1.Rem=Rem-Div | 0010 | 1110 1110
 | 2b: Rem<0 →+Div,sll R,R0=0 | 0010 | 0001 1100
2 | 1.Rem=Rem-Div | 0010 | 1111 1100
 | 2b: Rem<0 →+Div,sll R,R0=0 | 0010 | 0011 1000
3 | 1.Rem=Rem-Div | 0010 | 0001 1000
 | 2a: Rem>0 →sll R,R0=1 | 0010 | 0011 0001
4 | 1.Rem=Rem-Div | 0010 | 0001 0001
 | 2a: Rem>0 →sll R,R0=1 | 0010 | 0010 0011
 | Shift left half of Rem right 1 |  | 0001 0011

## Slide 82: Signed division
Keep the signs in mind for Dividend and Remainder
  (+ 7) ÷( + 2) = + 3 Remainder = +1
  7 = 3 × 2 + (+1) = 6 + 1
  (- 7 ) ÷(+ 2) = - 3 Remainder = -1
  -7 = -3 × 2 + (-1) = - 6 - 1
  (+ 7 ) ÷( - 2) = - 3 Remainder = +1
  (- 7 ) ÷( - 2) = + 3 Remainder = -1
One 64 bit register : Hi & Lo
  Hi: Remainder, Lo: Quotient
Instructions: div, divu
Divide by 0 → overflow : Check by software
Notes: Mflo, mfhi

## Slide 83: Faster Division
Can’t use parallel hardware as in multiplier
  Subtraction is conditional on sign of remainder
Faster dividers (e.g. SRT division) generate multiple quotient bits per step
  Still require multiple steps

## Slide 84: RISC-V Division
Four instructions:
  div, rem: signed divide, remainder
  divu, remu: unsigned divide, remainder
Overflow and division-by-zero don’t produce errors
  Just return defined results
  Faster for the common case of no error

## Slide 85: 3.6 Floating point numbers
Reasoning
  Larger number range than integer rage
  Fractions
  Numbers like e (2.71828) and π(3.14159265....)
Representation
  Sign
  Fraction
  Exponent
  More bits for fraction: more accuracy
  More bits for exponent: increases the range

## Slide 86: Floating Point
Representation for non-integral numbers
  Including very small and very large numbers
Like scientific notation
  –2.34 × 1056
  +0.002 × 10–4
  +987.02 × 109
In binary
  ±1.xxxxxxx2 × 2yyyy
Types float and double in C
normalized
not normalized

## Slide 87: Floating Point Standard
Defined by IEEE Std 754-1985
Developed in response to divergence of representations
  Portability issues for scientific code
Now almost universally adopted
Two representations
  Single precision (32-bit)
  Double precision (64-bit)

## Slide 88: IEEE Floating-Point Format
S: sign bit (0  non-negative, 1  negative)
Normalize significand: 1.0 ≤ |significand| < 2.0
  Always has a leading pre-binary-point 1 bit, so no need to represent it explicitly (hidden bit)
  Significand is Fraction with the “1.” restored
Exponent: excess representation: actual exponent + Bias
  Ensures exponent is unsigned
  Single: Bias = 127; Double: Bias = 1203
S
Exponent
Fraction
single: 8 bits double: 11 bits
single: 23 bits double: 52 bits

## Slide 89: Floating-Point Example
Represent –0.75
  –0.75 = (–1)1 × 1.12 × 2–1
  S = 1
  Fraction = 1000…002
  Exponent = –1 + Bias
    Single: –1 + 127 = 126 = 011111102
    Double: –1 + 1023 = 1022 = 011111111102
31 | 30 …… 23 | 22 …… 0
1 | 0111 1110 | 100 0000 0000 0000 0000 0000
1 bit | 8 bits | 23 bits
31 | 30 …… 20 | 19 …… 0
1 | 011 1111 1110 | 1000 0000 0000 0000 0000
1bit | 11 bits | 20 bits
0000 0000 0000 0000 0000 0000 0000 0000 |  | 
Double precision
Single precision

## Slide 90: Converting Binary to Decimal Floating Point
31 | 30 …… 23 | 22 …… 0
1 | 1000 0001 | 010 0000 0000 0000 0000 0000
1 bit | 8 bits | 23 bits

## Slide 91: Single-Precision Range
Exponents 00000000 and 11111111 reserved
Smallest value
  Exponent: 00000001  actual exponent = 1 – 127 = –126
  Fraction: 000…00  significand = 1.0
  ±1.0 × 2–126 ≈ ±1.2 × 10–38
Largest value
  exponent: 11111110  actual exponent = 254 – 127 = +127
  Fraction: 111…11  significand ≈ 2.0
  ±2.0 × 2+127 ≈ ±3.4 × 10+38

## Slide 92: Double-Precision Range
Exponents 0000…00 and 1111…11 reserved
Smallest value
  Exponent: 00000000001  actual exponent = 1 – 1023 = –1022
  Fraction: 000…00  significand = 1.0
  ±1.0 × 2–1022 ≈ ±2.2 × 10–308
Largest value
  Exponent: 11111111110  actual exponent = 2046 – 1023 = +1023
  Fraction: 111…11  significand ≈ 2.0
  ±2.0 × 2+1023 ≈ ±1.8 × 10+308
Notes: Exponent: 1~2046

## Slide 93: Floating-Point Precision
Relative precision
  all fraction bits are significant
  Single: approx 2–23
    Equivalent to 23 × log102 ≈ 23 × 0.3 ≈ 6 decimal digits of precision
  Double: approx 2–52
    Equivalent to 52 × log102 ≈ 52 × 0.3 ≈ 16 decimal digits of precision

## Slide 94: Denormal Numbers
Exponent = 000...0  hidden bit is 0
Smaller than normal numbers
  allow for gradual underflow, with diminishing precision
Denormal with fraction = 000...0
Two representations of 0.0!

## Slide 95: Infinities and NaNs
Exponent = 111...1, Fraction = 000...0
  ±Infinity
  Can be used in subsequent calculations, avoiding need for overflow check
Exponent = 111...1, Fraction ≠ 000...0
  Not-a-Number (NaN)
  Indicates illegal or undefined result
    e.g., 0.0 / 0.0
  Can be used in subsequent calculations

## Slide 96: Limitations
Overflow:
The number is too big to be represented
Underflow:
The number is too small to be represented

## Slide 97: IEEE 754 standard
00... 00two represents 0;
instead of interrupting on a divide by 0, software can set the result to a bit pattern representing +∞ or -∞;
NaN: Not a Number.
 - represented by f=0, E=255, S=0,1 - must obey all mathematical conventions: F+=, F/=0
denormalized numbers - represented by E=0 -values smaller than smallest normalized number - lowering probability of exponent underflow
Single precision |  | Double precision |  | Object represented
Exponent | Fraction | Exponent | Fraction | 
0 | 0 | 0 | 0 | 0
0 | Nonzero | 0 | Nonzero | denormalized number
1-254 | Anything | 1-2046 | Anything | Floating-point number
255 | 0 | 2047 | 0 | infinity
255 | Nonzero | 2047 | Nonzero | NaN (Not a Number)

## Slide 98: Floating point addition
Alignment
The proper digits have to be added
Addition of significands
Normalization of the result
Rounding
Example in decimal
system precision 4 digits
What is 9.999 • 101 + 1.610 • 10-1 ?

## Slide 99: Example for Decimal
Aligning the two numbers
9.999 •101
0.01610 •101 → 0.016 •101 Truncation
Addition
9.999 • 101
+ 0.016 • 101
10.015 • 101
Normalization
1.0015 • 102
Rounding
1.002 • 102
Notes: Truncation=舍去

## Slide 100: Algorithm
Normalize Significands
Add Significands
Normalize the sum
Over/underflow
Rounding
Normalization

## Slide 101: Example y=0.5+(-0.4375) in binary
0.510 = 1.0002×2-1
-0.43752=-1.1102×2-2
Step1:The fraction with lesser exponent is shifted right until matches
      -1.1102×2-2 → -0.1112×2-1
Step2: Add the significands
    1.0002×2-1
  +) - 0.1112×2-1
  0.0012×2-1
Step3: Normalize the sum and checking for overflow or underflow
    0.0012×2-1 → 0.0102×2-2 → 0.1002×2-3 → 1.0002×2-4
Step4: Round the sum
    1.0002×2-4 = 0.062510

## Slide 102: Algorithm

## Slide 103: Multiplication
Composition of number from different parts → separate handling
(s1 • 2e1) • (s2 • 2e2) = (s1 • s2) • 2e1+ e2
Example
1 10000010 000 0000 0000 0000 0000 0000 = -1 × 23
0 10000011 000 0000 0000 0000 0000 0000 = 1 × 24
Both significands are 1 → product = 1 →Sign=1
Add the exponents, bias = 127
        10000010
        +10000011
        110000101
Correction: 110000101-01111111=10000110=134=127+3+4
The result: 1 10000110 000 0000 0000 0000 0000 0000 = -1 × 27

## Slide 104: Multiplication
Add exponents
Multiply the significands
Normalize
Over- underflow
Rounding
Sign

## Slide 105: Data Flow

## Slide 106: multiplying the numbers 0.5ten and -0.4375ten →1.000twox 2-1 by -1.110twox 2-2
Step1:Adding the exponents without bias or using the biased
  -1 + (-2)=-3
  (-1 + 127) + (-2 + 127) - 127 = (-1 - 2) + (127 + 127-127) =-3+127 = 124
Step 2. Multiplying the significands
  1.110000twox2-3
Step 3. normalize
  127 ≥ -3 ≥ -126, no overflow or underflow.
Step 4. Rounding
  1.110twox2-3
Step 5. sign
  -1.110twox2-3 =-0.21875ten

## Slide 107: Division-- Brief
Subtraction of exponents
Division of the significands
Normalization
Rounding
Sign

## Slide 108: Parallelism and Computer Arithmetic: Associativity
x + (y+ z) = (x + y) + z ?
  x = -1.5ten x 1038, y= 1.5ten X 1038, and z = 1.0
  x + (y + z) = 0.0
  (x+y) + z = 1.0

## Slide 109: IEEE 754 standard
Rounding: four rounding modes
  Round to 0
  Round to +∞
  Round to -∞
  Round to next even number (default)

## Slide 110: Round modes
y | round down (towards −∞) | round up (towards +∞) | round towards zero | round to nearest even
+23.67 | +23 | +24 | +23 | +24
+23.50 | +23 | +24 | +23 | +24
+23.35 | +23 | +24 | +23 | +23
+23.00 | +23 | +23 | +23 | +23
0 | 0 | 0 | 0 | 0
−23.00 | −23 | −23 | −23 | −23
−23.35 | −24 | −23 | −23 | −23
−23.50 | −24 | −23 | −23 | −24
−23.67 | −24 | −23 | −23 | −24

## Slide 111: Accurate Arithmetic
IEEE 754 always keeps two extra bits on the right during intermediate additions, called guard and round
Rounding with Guard Digits
  Add 2.56ten x 100 to 2.34ten x 102
  The guard digit holds 5 and the round digit holds 6.
  Sum=2.37ten x 102.
Rounding without Guard Digits
  Sum=2.36ten x 102

## Slide 112: sticky bit
A bit used in rounding in addition to guard and round that is set whenever there are nonzero bits to the right of the round bit.
allows the computer to see the difference between 0.50 ... 00ten and 0.50 ... 0lten when rounding.
examples in the floating point format with guard, round and sticky bits
Notes: Guard, rounding, sticky bit

## Slide 113: Examples for guard, round, and sticky bit
g r s
1.11000000000000000000100 0 0 0
1.11000000000000000000100 (mantissa used, exact representation)
1.11000000000000000000000 1 1 0
1.11000000000000000000001
1.11000000000000000000000 0 1 0
1.11000000000000000000000
1.11000000000000000000000 1 1 1
1.11000000000000000000001
1.11000000000000000000000 0 0 1
1.11000000000000000000000
1.11000000000000000000000 1 0 0 (the “halfway” case) 1.11000000000000000000000 （LSB=0）
1.11000000000000000000001 1 0 0 (the “halfway” case) 1.11000000000000000000010（LSB=1）

## Slide 114: Concluding Remarks
Bits have no inherent meaning
  Interpretation depends on the instructions applied
Computer representations of numbers
  Finite range and precision
  Need to account for this in programs

## Slide 115: Concluding Remarks
ISAs support arithmetic
  Signed and unsigned integers
  Floating-point approximation to reals
Bounded range and precision
  Operations can overflow and underflow

## Slide 116
END