## Slide 1: Computer Organization & Design The Hardware/Software Interface
计算机组成与设计
Chapter 4
The processor
Part 1

## Slide 2: Computer Organization
Computer
CPU
Memory
I/O interface
Control unit
Datapath
Path: multiplexors
ALU
Registers
……

## Slide 3: Contents
Introduction & Logic Design Conventions
Building a datapath
A Simple Implementation Scheme
Pipelining

## Slide 4: 4.1 Introduction
CPU performance factors
  Instruction count
    Determined by ISA and compiler
  CPI and Cycle time
    Determined by CPU hardware
We will examine two RISC-V implementations
  A simplified version
  A more realistic pipelined version
Simple subset, shows most aspects
  Memory reference: ld, sd
  Arithmetic/logical: add, sub, and, or
  Control transfer: beq

## Slide 5: Instruction Execution Overview
For every instruction, the first two step are identical
    Fetch the instruction from the memory
    Decode and read the registers
  Next steps depend on the instruction class
    Memory-reference Arithmetic-logical branches
Depending on instruction class
  Use ALU to calculate
    Arithmetic result
    Memory address for load/store
    Branch comparison
  Access data memory for load/store
  PC  target address or PC + 4

## Slide 6: Simple Implementation
Include the functional units we need for each instruction
Why do we need this stuff?
A
L
U
c
o
n
t
r
o
l
R
e
g
W
r
i
t
e
R
e
g
i
s
t
e
r
s
W
r
i
t
e
r
e
g
i
s
t
e
r
R
e
a
d
d
a
t
a
1
R
e
a
d
d
a
t
a
2
R
e
a
d
r
e
g
i
s
t
e
r
1
R
e
a
d
r
e
g
i
s
t
e
r
2
W
r
i
t
e
d
a
t
a
A
L
U
r
e
s
u
l
t
A
L
U
D
a
t
a
D
a
t
a
R
e
g
i
s
t
e
r
n
u
m
b
e
r
s
a
.
R
e
g
i
s
t
e
r
s
b
.
A
L
U
Z
e
r
o
5
5
5
3

## Slide 7: ALU
算术逻辑运算器ALU：即运算器
  5 Operations
  “Set on less than”：
  if A<B then Result=1；
  else Result=0。
Operation | Function
000 | And
001 | Or
010 | Add
110 | Sub
111 | Slt
Less
Binvert
Operation
CarryIn
CarryOut
Result
A
B
00
01
10
11
0
1
3
ALU
Operation
A
Result
32
B
32

## Slide 8: ALU Control
ALUop与Func联合对ALU的控制

## Slide 9: ALU Control
ALU控制：
  ALU由ALUcontrol控制：ALUcontrol由ALUop和指令的低6位(5-0)联合产生ALU控制码。
  这样的好处在于分级控制，对于用的最多的加、减操作，系统只需给出两位的ALUop即可。
Result
Operation
ALUop
ALU
control
Func
[5-0]
32
A
ALU
32
3
2
32
B
zero

## Slide 10: REGISTER
Register
  State element。
  Can be controled by Write signal.
Register
In
Out
Register
In
Out
Write
Read：
Out=Register
Write：
Register=In
Clock cycle

## Slide 11: Memory
存储器：
  可分为指令存储器与数据存储器；
  指令存储器设为只读；输入指令地址，输出指令。
  数据存储器可以读写，由MemRead和MemWrite控制。按地址读出数据输出，或将写数据写入地址所指存储器单元。
Instruction
Instruction
Address
Instruction
memory
MemWrite
Read
data
Address
Data
memory
Write
data
MemRead

## Slide 12: Register Files--Built using D flip-flops
  32 64-bit Registers；
  Input: 2 64-bit;
  Output: 64-bit data, 32-bit register number;
  Register write control。

## Slide 13: Register File: Read-Output
  Output from the register
5 bits
5 bits
5 bits
32 bits
64 bits
64 bits
Reg. address
Reg. address
Data output

## Slide 14: Register File: Write-Input
  Written to the register
64 bits
rd
5 bits
Reg. address
Write signals

## Slide 15
Description: 32×64bits Register files
Module regs(clk, rst,reg_Rd_addr_A, reg_Rt_addr_B, reg_Wt_addr, wdata, we, rdata_A, rdata_B);
input clk, rst, we;
input [4:0] reg_Rd_addr_A, reg_Rt_addr_B, reg_Wt_addr;
input [31:0] wdata;
output [31:0] rdata_A, rdata_B;
reg [31:0] register [1:31]; // r1 - r31
integer i;
assign rdata_A = (reg_Rd_addr_A == 0)? 0 : register[reg_Rd_addr_A]; // read
assign rdata_B = (reg_Rt_addr_B == 0)? 0 : register[reg_Rt_addr_B]; // read
always @(posedge clk or posedge rst)
begin
if (rst==1) begin // reset
for (i=1; i<32; i=i+1)
register[i] <= 0;
end
else begin
if ((reg_Wt_addr != 0) && (we == 1)) // write
register[reg_Wt_addr] <= wdata;
end
end
endmodule

## Slide 16: The other elements
Sign Extend：
  将16位的补码表示的有符号立即数，扩展为32位。
  方法：只需重复符号位即可。
Shift：
  Shift 2 bits left。
  方法：将输入高移2位接输出，输出的低两位接0。
16
32
Sign
extend
D15
D14
.
.
.
D00
D31
.
.
.
D16
D15
D14
.
.
.
D00
Shift
left 2
D31
D30
D29
.
.
.
.
.
.
D02
D01
D00
D31
D30
D29
.
.
.
.
.
.
D02
D01
D00

## Slide 17: CPU Overview

## Slide 18: Multiplexers
Can’t just join wires together
  Use multiplexers

## Slide 19: Control

## Slide 20: Logic Design Conventions
Information encoded in binary
  Low voltage = 0, High voltage = 1
  One wire per bit
  Multi-bit data encoded on multi-wire buses
Combinational element
  Operate on data
  Output is a function of input
State (sequential) elements
  Store information

## Slide 21: Clocking Methodology
An edge triggered methodology
Typical execution:
  read contents of some state elements,
  send values through some combinational logic
  write results to one or more state elements

## Slide 22: Contents
Introduction & Logic Design Conventions
Building a datapath
A Simple Implementation Scheme
Pipelining
Exceptions

## Slide 23: 4.3 Building a datapath
Datapath
  Elements that process data and addresses in the CPU
    Registers, ALUs, mux’s, memories, …
We will build a RISC-V datapath incrementally
  Refining the overview design

## Slide 24: RISC-V fields (format)
opcode：basic operation of the instruction.
rs1： the first register source operand.
rs2： the second register source operand.
rd： the register destination operand.
funct： function,this field selects the specific variant of the operation in the op field.
Immediate: address or immediate

## Slide 25
Name | Register name | Usage | Preserved On call?
x0 | 0 | The constant value 0 | n.a.
x1(ra) | 1 | Return address(link register) | yes
x2(sp) | 2 | Stack pointer | yes
x3(gp) | 3 | Global pointer | yes
x4(tp) | 4 | Thread pointer | yes
x5-x7 | 5-7 | Temporaries | no
x8-x9 | 8-9 | Saved | yes
x10-x17 | 10-17 | Arguments/results | no
x18-x27 | 18-27 | Saved | yes
x28-x31 | 28-31 | Temporaries | no
Name | Example | Comments
32 registers | x0-x31 | Fast locations for data. In RISC-V, data must be in registers to perform arithmetic. Register x0 always equals 0.
261 memory words | Memory[0], Memory[8] , …… , Memory[18446744073709551608] | Accessed only by data transfer instructions. RISC-V uses byte addresses, so sequential doubleword accesses differ by 8. Memory holds data structures, arrays, and spilled registers.

## Slide 26: RISC-V assembly language
Category | Instruction | Example | Meaning | Comments
Arithmetic | add | add x5,x6,x7 | x5=x6 + x7 | Add two source register operands
 | subtract | sub x5,x6,x7 | x5=x6 - x7 | First source register subtracts second one
 | add immediate | addi x5,x6,20 | x5=x6+20 | Used to add constants
Data transfer | load doubleword | ld x5, 40(x6) | x5=Memory[x6+40] | doubleword from memory to register
 | store doubleword | sd x5, 40(x6) | Memory[x6+40]=x5 | doubleword from register to memory
Logical | and | and x5, x6, 3 | x5=x6 & 3 | Arithmetic shift right by register
 | inclusive or | or x5,x6,x7 | x5=x6 ¦ x7 | Bit-by-bit OR
Conditional Branch | branch if equal | beq x5, x6, 100 | if(x5 == x6) go to PC+100 | PC-relative branch if registers equal
 | branch if not equal | bne x5, x6, 100 | if(x5 != x6) go to PC+100 | PC-relative branch if registers not equal
Unconditional Branch | jump and link | jal x1, 100 | x1 = PC + 4; go to PC+100 | PC-relative procedure call
 | jump and link register | jalr x1, 100(x5) | x1 = PC + 4; go to x5+100 | procedure return; indirect call

## Slide 27: Instruction execution in RISC-V
Fetch :
  Take instructions from the instruction memory
  Modify PC to point the next instruction
Instruction decoding & Read Operand:
  Will be translated into machine control command
  Reading Register Operands, whether or not to use
Executive Control:
  Control the implementation of the corresponding ALU operation
Memory access:
  Write or Read data from memory
  Only ld/sd
Write results to register:
  If it is R-type instructions, ALU results are written to rd
  If it is I-type instructions, memory data are written to rd

## Slide 28: Instruction fetching three elements
PC
Add
Instruction memory
Program counter
Adder
How to connect? Who?
Data Stream of Instruction fetching
Read address
Instruction
Instruction
Memory

## Slide 29: Instruction fetching unit
PC
4
CPU
Read address
Instruction
Instruction
Memory
add
Instruction
Instruction Register
  Can you omit it?

## Slide 30: How simple is!
Why PC+4?

## Slide 31: More Implementation Details
Abstract / Simplified View:

## Slide 32: Path Built using Multiplexer
R-type instruction Datapath
I-type instruction Datapath
  For ALU
  For load
S-type (store) instruction Datapath
SB-type (branch) instruction Datapath
UJ-type instruction Datapath
  For Jump
First, Look at the data flow within instruction execution
Data Stream of Instruction executing

## Slide 33: R type Instruction & Data stream
op(7)
rd(5)
func3
rs1(5)
rs2(5)
func7
rs1
rs2
rd
ins20-24
ins15-19
Registers
Read reg. address1
Read reg. address2
Write reg. address
Write data
Read data1
Read data2
ALU result
Zero
ALU
4
RegWrite
ALU operation
ins7-11
control
64bits data
ALUC
add x9, x20, x21
Read two register operands
Perform arithmetic/logical operation
Write register result

## Slide 34: I type (load) Instruction & Data stream
rs1
rs2
rd
Registers
Read reg. address1
Read reg. address2
Write reg. address
Write data
Read data1
Read data2
ALU result
Zero
ALU
4
RegWrite
ALU operation
control
address
Write data
Read data
Sign extend
ins7-11
ins0-31
MemWrite
MemRead
32
64
64bits data
ld x1, 200(x2)
Data
Memory
ALUC
ALUop
op(7)
rd(5)
func3
rs1(5)
Immediate(12)
ins15-19
Read register operands
Calculate address using 12-bit offset
  Use ALU, but sign-extend offset
Read memory and update register
addi x1, x2，4？

## Slide 35: S-type (store) Instruction & Data stream
rs1
rs2
rd
Registers
Read reg. address1
Read reg. address2
Write reg. address
Write data
Read data1
Read data2
ALU result
Zero
ALU
4
RegWrite
ALU operation
control
address
Write data
Read data
Sign extend
ins0-31
MemWrite
MemRead
32
64
sd x1, 200(x2)
Data
Memory
ALUC
ALUop
ins15-19
Read register operands
Calculate address using 12-bit offset
  Use ALU, but sign-extend offset
Write register value to memory
op(7)
imm5
func3
rs1(5)
rs2(5)
imm7
ins20-24

## Slide 36: SB type Instruction & Data stream of beq
rs1
rs2
Registers
Read reg. address1
Read reg. address2
Write reg. address
Write data
Read data1
Read data2
ALU result
Zero
ALU
3
RegWrite
ALU operation
Sign extend
32
64
Shift
left 1
PC+4 from instruction
ADD
To PC
control
ALUC
Branch
ALUop
op(7)
imm5
func3
rs1(5)
rs2(5)
imm7
Read register operands
Compare operands
  Use ALU, subtract and check Zero output
Calculate target address
  Sign-extend displacement
  Shift left 1 place (halfword displacement)
  Add to PC value
beq x1, x2，200
ins15-19
ins20-24
ins0-31

## Slide 37: UJ type Instruction
rs
rt
Registers
Read reg. address1
Read reg. address2
Write reg. address
Write data
Read data1
Read data2
ALU result
Zero
ALU
3
RegWrite
ALU operation
Sign extend
bit0-15
bit21-25
bit16-20
16
32
Shift
left 2
ADD
To PC
control
Branch
PC+4[31:28]##bit25-00##00
Jump
bit25-00
Shift left 2
##
28
PC+4[31:28]
bit25-00##00
Op(7)
rd(5)
Target address(20)
jal x1, procedure

## Slide 38: Composing the Elements
First-cut data path does an instruction in one clock cycle
  Each datapath element can only do one function at a time
  Hence, we need separate instruction and data memories
Use multiplexers where alternate data sources are used for different instructions

## Slide 39: R-Type/Load/Store Datapath

## Slide 40: Full Datapath

## Slide 41: Full datapath
Registers
Read address1
Read address2
Write address
Write data
Read data1
Read data2
ALU
result
Zero
ALU
3
RegWrite
address
Write data
Read data
Sign extend
ins0-31
ins15-19
ins20-24
MenWrite
MenRead
32
64
64bits data
MUX
ins7-11
MUX
ALU operation
Shift
left 1
MUX
ADD
ADD
PC
Data
Memory
Read address
Instruction
Instruction
Memory
4
Instruction
R

## Slide 42: Full datapath
Registers
Read address1
Read address2
Write address
Write data
Read data1
Read data2
ALU
result
Zero
ALU
3
RegWrite
address
Write data
Read data
Sign extend
MenWrite
MenRead
32
64
64bits data
MUX
MUX
ALU operation
Shift
left 1
MUX
ADD
ADD
PC
Data
Memory
Read address
Instruction
Instruction
Memory
4
Instruction
I-LW
ins15-19
ins20-24
ins7-11
ins0-31

## Slide 43: Full datapath
Registers
Read address1
Read address2
Write address
Write data
Read data1
Read data2
ALU
result
Zero
ALU
3
RegWrite
address
Write data
Read data
Sign extend
MenWrite
MenRead
32
64
64bits data
MUX
MUX
ALU operation
Shift
left 1
MUX
ADD
ADD
PC
Data
Memory
Read address
Instruction
Instruction
Memory
4
Instruction
S-SW
ins15-19
ins20-24
ins7-11
ins0-31

## Slide 44: Full datapath
Registers
Read address1
Read address2
Write address
Write data
Read data1
Read data2
ALU
result
Zero
ALU
3
RegWrite
address
Write data
Read data
Sign extend
MenWrite
MenRead
32
64
64bits data
MUX
MUX
ALU operation
Shift
left 2
MUX
ADD
ADD
PC
Data
Memory
Read address
Instruction
Instruction
Memory
4
Instruction
B-beq
ins15-19
ins20-24
ins7-11
ins0-31

## Slide 45: Contents
Introduction & Logic Design Conventions
Building a datapath
A Simple Implementation Scheme
Pipelining

## Slide 46: Building the Datapath & Controller
There are 6+4 signals

## Slide 47: Building Controller
Analyse for cause and effect
Information comes from the 32 bits of the instruction
Selecting the operations to perform (ALU, read/write, etc.)
Controlling the flow of data (multiplexor inputs)
ALU's operation based on instruction type and function code

## Slide 48: Scheme of Controller
2-level decoder
First
Main
decoder
ALU
Decoder
Second
Control Signals (6)
opcode(7)
rd
funct(3)
rs1
rs2
funct(7)
ALU operation(4)
ALU op(2)
Defined
Defined

## Slide 49: The ALU control is where and other signals(6)
Output signals

## Slide 50: Signals for datapath Defined 6 control signals

## Slide 51: Designing the Main Control Unit First level
Main Control Unit function
  ALU op (2)
  Divided 6 control signals into 2 groups
    3 Mux
    3 R/W
control
Instruction opcode (7)
ALU op (2)
Mux (3)
R/W (3)
ALUScr
PCSrc
MemtoReg
MemRead
MemWrite
RegWrite
ld | 00
sd | 00
Beq | 01
R-type | 10

## Slide 52: Truth Table for Main decoder

## Slide 53: Truth tables & Circuitry of main Controller
输入 |  | 输出 |  |  |  |  |  |  |  | 
Instruction | OPCode | ALUSrcB | Memto-Reg | Reg Write | Mem Read | Mem Write | Branch | Jump | ALUOp1 | ALU Op0
R-format | 0110011 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0
Lw(I-Type) | 0000011 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0
sw(S-Type) | 0100011 | 1 | X | 0 | 0 | 1 | 0 | 0 | 0 | 0
beq(B-Type) | 1100111 | 0 | X | 0 | 0 | 0 | 1 | 0 | 0 | 1
Jal | 1101111 | X | X | 0 |  | 0 | 0 | 1 | X | X

## Slide 54: Main Controller Code

## Slide 55: Design the ALU Decoder second level
ALU used for
  Load/Store: F = add
  Branch: F = subtract
  R-type: F depends on funct field
ALU control lines | Function
0000 | AND
0001 | OR
0010 | add
0110 | subtract

## Slide 56: ALU Control
ALU operation is decided by 2-bit ALUOp derived from opcode, and funct7 & funct3 fields of the instruction
  Combinational logic derives ALU control
opcode | ALUOp | Operation | Funct7 field | Funct3 field | ALU action | ALU control
ld | 00 | load doubleword | XXXXXXX | XXX | add | 0010
sd | 00 | store doubleword | XXXXXXX | XXX | add | 0010
beq | 01 | branch if equal | XXXXXXX | XXX | subtract | 0110
R-type | 10 | add | 0000000 | 000 | add | 0010
 |  | subtract | 0100000 | 000 | subtract | 0110
 |  | AND | 0000000 | 111 | AND | 0000
 |  | OR | 0000000 | 110 | OR | 0001

## Slide 57: Truth Table for ALU decoder
Describe it using a truth table (can turn into gates):
don’t care

## Slide 58: The ALU control signals -- logic circuit
0 | x | x | 1
0 | 0 | 1 | x
x | x | x | x
x | x | x | 1
F1F0
F3F2
F1
1 | x | x | 1
0 | 0 | 0 | X
x | x | x | X
1 | x | x | 1
F1F0
F3F2
F2
0 | x | x | 0
0 | 1 | 0 | X
x | x | x | X
x | x | x | 1
F1F0
F3F2
F0F1
F3

## Slide 59: ALU Controller Code

## Slide 60: R-Type Instruction

## Slide 61: Load Instruction

## Slide 62: BEQ Instruction

## Slide 63: Single Cycle Implementation performance for lw
Calculate cycle time assuming negligible delays except:
  memory (200ps), ALU and adders (200ps), register file access (100ps)
200ps
200ps
200ps
100+100=200ps

## Slide 64: Performance in Single Cycle Implementation
Let’s see the following table:
The conclusion:
  Different instructions needs different time.
  The clock cycle must meet the need of the slowest instruction. So, some time will be wasted.
Let’s see the following table:
Instr | Instr fetch | Register read | ALU op | Memory access | Register write | Total time
ld | 200ps | 100 ps | 200ps | 200ps | 100 ps | 800ps
sd | 200ps | 100 ps | 200ps | 200ps |  | 700ps
R-format | 200ps | 100 ps | 200ps |  | 100 ps | 600ps
beq | 200ps | 100 ps | 200ps |  |  | 500ps

## Slide 65: Performance Issues
Longest delay determines clock period
  Critical path: load instruction
  Instruction memory  register file  ALU  data memory  register file
Wasteful of area. If the instruction needs to use some functional unit multiple times.
  E.g., the instruction ‘mult’needs to use the ALU repeatedly. So, the CPU will be very large.
Violates design principle
  Making the common case fast
We will improve performance by pipelining

## Slide 66
END

## Slide 67: j instruction
instruction format
  j Label
Implementation
  pc = pc28~31 ## 26bits-address × 4
000010/2
26 bits address

## Slide 68: The Datapath in operation for Jump
Registers
0
M
U
X
1
ALU
control
0
M
U
X
1
Read
data 2
Zero
Read
register 1
Read
data 1
Read
register 2
Add
ALU
result
Data
memory
Sign
extend
Instruction [25-21]
Instruction [15-0]
16
32
Instruction [20-16]
ALU
Shift
left 2
I-type |  |  | 
Op | rs | rt | Immediate
Write
data
Address
ALU
result
Read
data
0
M
U
X
1
Write
register
Write
data
0
M
U
X
1
Instruction [15-11]
Instruction [5-0]
R-type |  |  |  |  | 
Op | rs | rt | rd | shamt | Funct
Control
RegDst
Branch
MemRead
MemtoRead
ALUOp
MemWrite
ALUSrc
RegWrite
1
M
U
X
0
jump
jump instruction
Instruction
memory
Jump-type | 
Op | address
28
Shift
left 2
Instruction [25-0]
jump address[31-0]
PC+4[31-28]
Instruction [31-26]
26
Read
address
Instruction
[31-0]
Add
pc
4